MD simulation of GemPi1kda in water
All-atom simulation
Model
Gempi1kda.cdx → gempi1kda_GMX.gro and gempi1kda_GMX.itp (gempi1kda.acpype)

Setup
### ./setup.sh ###
# Place the solute in a simulation box
gmx editconf -f gempi1kda_GMX.gro -bt cubic -d 1.4 -o gempi1_inbox.gro

# Prepare minimization in vacuum
gmx grompp -f em_vacuum.mdp -c gempi1_inbox.gro -p topol.top -o em_vacuum.tpr

# Make minimization in vacuum
gmx mdrun -s em_vacuum.tpr -deffnm em_vacuum -v

# Fill the box with water
gmx solvate -cp em_vacuum.gro -cs spc216.gro -o gempi1_inslv.gro -p topol.top

# Prepare the minimization in the solvent
gmx grompp -f em_solvent.mdp -c gempi1_inslv.gro -p topol.top -o em_solvent.tpr

# Make minimzation in the solvent
gmx mdrun -s em_solvent.tpr -deffnm em_solvent -v

Equil
### ./equil.sh ###
# Prepare Berendsen equilibration
gmx grompp -f berendsen.mdp -c em_solvent.gro -p topol.top -o berendsen.tpr

# Make Berendsen equilibration
gmx mdrun -s berendsen.tpr -deffnm berendsen -v

# Prepare Nose-Hoover equilibration
gmx grompp -f nosehoover.mdp -c berendsen.gro -p topol.top -o nosehoover.tpr

# Make Nose-Hoover equilibration
gmx mdrun -s nosehoover.tpr -deffnm nosehoover -v

Prod
### nohup ./prod.sh & ###
# Prepare production run
gmx grompp -f md_prod.mdp -c nosehoover.gro -p topol.top -o md_prod.tpr

# Make production run
gmx mdrun -s md_prod.tpr -deffnm md_prod -v

### ./rstr.sh ###
# Restart production run
gmx mdrun -s md_prod.tpr -deffnm md_prod -v -cpi md_prod.cpt

Parametrizing a new molecule based on atomistic simulations
Choose an atom-to-bead mapping, create mapping.ndx file

Put the GemPi1kda into the center of box and generated .gro and .xtc files
#### ./extr.sh ###
gmx trjconv -f nosehoover.gro -s md_prod.tpr -o md_solute.gro -center -pbc cluster

gmx trjconv -f md_prod.xtc -s md_prod.tpr -o md_solute.xtc -center -pbc cluster

Coarse-grain target atomistic data.
Create a .itp index file with a directive for "[bonds]" containing (multiple) pairs of CG beads, "[angles]" containing triples and "[dihedrals]" quartets.
        ### ./mapped.sh ###
Seq 0 22 ∣gmx traj -f md_solute.gro -s md_solute.tpr -oxt md_mapped.gro -n mapping.ndx -com -ng 23
Seq 0 22 ∣gmx traj -f md_solute.xtc -s md_solute.tpr -oxt md_mapped.xtc -n mapping.ndx -com -ng 23
gmx grompp -f 1kda_minim.mdp -c md_mapped.gro -p 1kda_mapped.top -o 1kda_mapped.tpr

Calculate the average and standard deviation for all the distributions (bond angle …)
creat bonds.ndx and angles.ndx
### ./bondanalysis.sh ###
rm -rf BONDDISTRIBUTIONS
mkdir BONDDISTRIBUTIONS

NBONDS=24

IBOND=0
while [ $IBOND -lt $NBONDS ]
    do
    echo $IBOND | gmx distance -f md_mapped.xtc -n bonds.ndx -s 1kda_mapped.tpr -oall BONDDISTRIBUTIONS/bond_$IBOND.xvg
    gmx analyze -f BONDDISTRIBUTIONS/bond_$IBOND.xvg -dist BONDDISTRIBUTIONS/distr_$IBOND.xvg -bw 0.01
    rm -rf \#*
    let IBOND=$IBOND+1
    done
exit

### ./angleanalysis.sh ###
rm -rf ANGLEDISTRIBUTIONS
mkdir ANGLEDISTRIBUTIONS

NANGLES=31

IANGLE=0
while [ $IANGLE -lt $NANGLES ]
    do
    echo $IANGLE | gmx angle -f md_mapped.xtc -n angles.ndx -type angle -ov ANGLEDISTRIBUTIONS/angle_$IANGLE.xvg
    gmx analyze -f ANGLEDISTRIBUTIONS/angle_$IANGLE.xvg -dist ANGLEDISTRIBUTIONS/distr_$IANGLE.xvg -bw 1.0
    rm -rf \#*
    let IANGLE=$IANGLE+1
    done
exit

CG simulation
Create the CG itp file
We can use the itp file of all-atom simulation
Create CG simulation
Mkdir Take1, run CG simulation
### ./runcg.sh ###
gmx grompp -f minim.mdp -c init_cg.gro -p 1kda_mapped.top -o minimization.tpr
gmx mdrun -v -deffnm minimization

gmx grompp -f relax.mdp -c minimization.gro -p 1kda_mapped.top -o relax.tpr
gmx mdrun -v -deffnm relax

gmx grompp -f cg_md.mdp -c relax.gro -p 1kda_mapped.top -o cg_md.tpr
gmx mdrun -v -deffnm cg_md
Calculate the average and standard deviation for all the distributions
### ./DOBONDANALYSIS.sh ###
rm -rf BONDDISTRIBUTIONS
mkdir BONDDISTRIBUTIONS

NBONDS=24

IBOND=0
while [ $IBOND -lt $NBONDS ]
    do
    echo $IBOND | gmx distance -f cg_md.xtc -n bonds.ndx -s cg_md.tpr -oall BONDDISTRIBUTIONS/bond_$IBOND.xvg
    gmx analyze -f BONDDISTRIBUTIONS/bond_$IBOND.xvg -dist BONDDISTRIBUTIONS/distr_$IBOND.xvg -bw 0.01
    rm -rf \#*
    let IBOND=$IBOND+1
    done
sh
exit

### ./DOANGLEANALYSIS.sh ###
rm -rf ANGLEDISTRIBUTIONS
mkdir ANGLEDISTRIBUTIONS

NANGLES=31

IANGLE=0
while [ $IANGLE -lt $NANGLES ]
    do
    echo $IANGLE | gmx angle -f cg_md.xtc -n angles.ndx -type angle -ov ANGLEDISTRIBUTIONS/angle_$IANGLE.xvg
    gmx analyze -f ANGLEDISTRIBUTIONS/angle_$IANGLE.xvg -dist ANGLEDISTRIBUTIONS/distr_$IANGLE.xvg -bw 1.0
    rm -rf \#*
    let IANGLE=$IANGLE+1
    done

exit

Optimize CG bonded parameters
Change the value of bond, angle
length (peak altitude, the higher the bigger value)
force (peak width, the more width the less value)
Repeat ./runcg.sh until the value is more closed to the all-atom simulation

MD simulation of GemPi1kda in octanol
1. Model
Gempi1kda.cdx → gempi1kda_GMX.gro and gempi1kda_GMX.itp (gempi1kda.acpype)
octanol.cdx → octanol_GMX.gro and octanol_GMX.itp (octanol.acpype)
need generate the gro and itp files of octanol

2. Setup
   ### ./setup.sh ###
# Place the solute in a simulation box
gmx editconf -f gempi1kda_GMX.gro -bt cubic -d 1.4 -o gempi1_inbox.gro

# Prepare minimization in vacuum
gmx grompp -f em_vacuum.mdp -c gempi1_inbox.gro -p topol.top -o em_vacuum.tpr

# Make minimization in vacuum
gmx mdrun -s em_vacuum.tpr -deffnm em_vacuum -v

# Fill the box with water
gmx insert-molecules -f em_vacuum.gro -ci octanol_GMX.gro -o gempi1_inslv.gro -nmol 5000

# Prepare the minimization in the solvent
gmx grompp -f em_solvent.mdp -c gempi1_inslv.gro -p topol.top -o em_solvent.tpr

# Make minimzation in the solvent
gmx mdrun -s em_solvent.tpr -deffnm em_solvent -v

3. Equil
### ./equil.sh ###
# Prepare Berendsen equilibration
gmx grompp -f berendsen.mdp -c em_solvent.gro -p topol.top -o berendsen.tpr

# Make Berendsen equilibration
gmx mdrun -s berendsen.tpr -deffnm berendsen -v

# Prepare Nose-Hoover equilibration
gmx grompp -f nosehoover.mdp -c berendsen.gro -p topol.top -o nosehoover.tpr

# Make Nose-Hoover equilibration
gmx mdrun -s nosehoover.tpr -deffnm nosehoover -v

4. Prod
### ./prod.sh ###
# Prepare production run
gmx grompp -f md_prod.mdp -c nosehoover.gro -p topol.top -o md_prod.tpr

# Make production run
gmx mdrun -s md_prod.tpr -deffnm md_prod -v

### ./rstr.sh ###
# Restart production run
gmx mdrun -s md_prod.tpr -deffnm md_prod -v -cpi md_prod.cpt

5. Put the GemPi1kda into the center of box and generate .gro and .xtc files
### ./estr.sh ###
gmx convert-tpr -s md_prod.tpr -o md_solute.tpr

gmx trjconv -f nosehoover.gro -s md_prod.tpr -o md_solute.gro -center -pbc cluster

gmx trjconv -f md_prod.xtc -s md_prod.tpr -o md_solute.xtc -center -pbc cluster

6. Coarse-grain target atomistic data.
Create a .itp index file with a directive for "[bonds]" containing (multiple) pairs of CG beads, "[angles]" containing triples and "[dihedrals]" quartets.

### ./mapp.sh ###
seq 0 22 | gmx traj -f md_solute.gro -s md_solute.tpr -oxt md_mapped.gro -n mapping.ndx -com -ng 23

seq 0 22 | gmx traj -f md_solute.xtc -s md_solute.tpr -oxt md_mapped.xtc -n mapping.ndx -com -ng 23

gmx grompp -f 1kda_minim.mdp -c md_mapped.gro -p 1kda_mapped.top -o 1kda_mapped.tpr

Calculate the average and standard deviation for all the distributions (bond, angle …)
Creat bond.ndx and angle.ndx
### ./bondanalysis.sh ###
rm -rf BONDDISTRIBUTIONS
mkdir BONDDISTRIBUTIONS

NBONDS=24

IBOND=0
while [ $IBOND -lt $NBONDS ]
    do
    echo $IBOND | gmx distance -f md_mapped.xtc -n bonds.ndx -s 1kda_mapped.tpr -o all BONDDISTRIBUTIONS/bond_$IBOND.xvg
    gmx analyze -f BONDDISTRIBUTIONS/bond_$IBOND.xvg -dist BONDDISTRIBUTIONS/distr_$IBOND.xvg -bw 0.01
    rm -rf \#*
    let IBOND=$IBOND+1
    done

exit

 ### ./angleanalysis.sh ###
rm -rf ANGLEDISTRIBUTIONS
mkdir ANGLEDISTRIBUTIONS

NANGLES=31

IANGLE=0
while [ $IANGLE -lt $NANGLES ]
    do
    echo $IANGLE | gmx angle -f md_mapped.xtc -n angles.ndx -type angle -ov ANGLEDISTRIBUTIONS/angle_$IANGLE.xvg
    gmx analyze -f ANGLEDISTRIBUTIONS/angle_$IANGLE.xvg -dist ANGLEDISTRIBUTIONS/distr_$IANGLE.xvg -bw 1.0
    rm -rf \#*
    let IANGLE=$IANGLE+1
    done

exit

6. CG simulation
Create the CG itp file
We can use the itp file of CG simulation in water
Mapping Octanol beads and GemPi1kda beads
For each octanol, there are 2 beads in one molecular
### indexer.py ###
#!/usr/bin/env python

nmols = 1138 # Number of molecules
atspermol = 9 # AA atoms per molecule
beadspermol = 2 # CG beads per molecule
firstbead = 4 # AA atoms in the first bead
atsperbead = 4 # AA atoms per CG bead
lastbead = 5 # AA atoms in the last bead

outname = "mapping.ndx" # Output filename

with open(outname,'w') as NDX:
    for mol in range(nmols):
        for bead in range(beadspermol):

        # The number of atoms (nats) might depend on whether it's a first,
        # last, or middle bead. NDXs are 1-based
        if bead==0:
        nats = firstbead
        startat = 1
        elif bead==beadspermol-1:
        nats = lastbead
        startat = atspermol-lastbead+1
        else:
        nats = atsperbead
        startat = (bead-1)*atsperbead + firstbead + 1

        startat += mol*atspermol
        ats = range(startat, startat + nats)
        ats = " ".join(map(str, ats))
        NDX.write("[ mol%dbead%d ]\n%s\n" % (mol+1,bead+1, ats))

7. Mapping all the octanol beads into the gro file
### ./mapp.sh ###
seq 0 2275 | gmx traj -f octanolnoh.gro -s octanolnoh.gro -oxt cg_octanol.gro -n mapping.ndx -com -ng 2276
where 2275 is the number of CG beads in your molecule and the 'seq 0 2274' avoids having to type all index groups. Inspect the file mapping.ndx to see how the atoms of toluene are grouped into the CG beads

8. put cg_gempi1kda.gro and cg_octanol.gro into the same cg_gemocta.gro, and edit cg_gemocta.gro, detect the line between two files
### ./mono.sh ###
#!/bin/bash
cat cg_gempi1kda.gro cg_octanol.gro > cg_gemocta.gro
edit cg_gemocta.gro

9.  Create CG simulation
Extract one frame from your mapped trajectory and solvate it in the same solvent as the atomistic simulation. Create a top file (include the general martini itp files and the newly created molecule itp and add the right number of molecules (solute and solvent))
We can use the itp file of all-atom simulation in octanol
### ./cgmd.sh ###
### minimization ###
gmx grompp -f minim.mdp -c cg_gemocta.gro -p cg_gemocta.top -o minim.tpr
gmx mdrun -v -deffnm minim
(if the atom is not cooperated, run the commands below)
gmx grompp -f minim.mdp -c cg_gemocta.gro -p cg_gemocta.top -o minim.tpr -maxwarn 10)

### relax the trajectory in the same solvent ###
gmx grompp -f relax.mdp -c minim.gro -p cg_gemocta.top -o relax.tpr
gmx mdrun -v -deffnm relax

### run MD simulation ###
gmx grompp -f cg_md.mdp -c relax.gro -p cg_gemocta.top -o cg_md.tpr
gmx mdrun -v -deffnm cg_md

10. Calculate the average and standard deviation for all the distributions
### ./bondanalysis.sh ###
### ./angleanalysis.sh ###

11. Analyze the bond distribution and angle distribution, change the value of itp files, repeat step 9 until get a good result.

After we get a good itp file, we use it to simulate 24 GemPi1kda in the box to explore the aggregation of them.
3. ProDrug-subject MAE abstract
Coarse-grained MD simulation of GemPi1kda in solution (Water+150mM NaCl)

Conditions:
- 150mM NaCl + water
- 1mM ProDrug (1kda)
- 325140 beads with Martini V2.1_dna FF
- 1microsecond expected

Preparing step
a. Here we used the optimised itp obtained from multiple coarsed-grained MD simulations of 1 GemPi1kda in octonol, here the selected parameters from simulation #6.(Copy cg_md.xtc and cg_md.tpr from ~/ProDrug/Octanol/Take11 )

# GemPi1kda has been extract from the last frame ~ 5000 ps, choose #2 – non.
gmx trjconv -f cg_md.xtc -s cg_md.tpr -o prodrug.gro

( gmx trjconv -f cg_md.xtc -s cg_md.tpr -dump 700000 -o prodrug.gro )

b. Then using some unix routines, we replicate the chain until 24 polymers into the box. The box size has been fix at ~ 34.16nm for x,y,z dimensions for a concentration of [ProDrug] at 1mM.

# Place the solute in a simulation box
gmx editconf -f prodrug.gro -bt cubic -d 1 -o prodrug_inbox.gro

# put additional 23 prodrug in the box
gmx insert-molecules -f prodrug_inbox.gro -ci prodrug.gro -o system0.gro -nmol 23 -box 32 32 32

# define the size of box
gmx editconf -f system0.gro -o system_temp.gro -d 1.0 -bt cubic -box 34.16 34.16 34.16

Minimization steps
# Minimization in vaccum following by minimization in solution
gmx grompp -f minimization-vac.mdp -c system_temp.gro -p system.top -o minimization-vac.tpr
gmx mdrun -deffnm minimization-vac -v

# Solvatation
gmx solvate -cp minimization-vac.gro -cs water.gro -radius 0.21 -o system_W.gro

gmx grompp -f ions.mdp -c system_W.gro -p system_1.top -o ions.tpr

# Add ions into the box
gmx genion -s ions.tpr -p system_2.top -neutral -conc 0.15 -pname NA+ -nname CL- -o system_WI.gro -n ion.ndx
Then select the water group, here it’s the #3.

# minimization
gmx grompp -f minimization.mdp -c system_WI.gro -p system_2.top -o minimization.tpr
gmx mdrun -deffnm minimization -v

Equilibration and production step
Set 50000 step for the equilibration following by 1µs of production
nohup ./run_ProDrug.sh > run_ProDrug.out & (4 days)

# Equil
gmx grompp -f equilibration.mdp -c minimization.gro -p system.top -o equilibration.tpr -n system.ndx
gmx mdrun -deffnm equilibration -v

# Prod
gmx grompp -f dynamic.mdp -c equilibration.gro -p system.top -o dynamic.tpr -n system.ndx
gmx mdrun -deffnm dynamic -v

4.increase the simulation from 5us to 10us
edit new tpr file
① gmx convert-tpr -s dynamic3.tpr -o dynamic.tpr -extend 5000000
    gmx convert-tpr -s dynamic3.tpr -o dynamic.tpr -until 10000000
or
a, motified the nstep in dynamic.mdp, change steps from 50000000 to 250000000

b. cp dynamic.cpt dynamic0.cpt
    cp dynamic.tpr dynamic0.tpr
     cp run_ProDrug.out run_ProDrug0.out

②run the run_ProDrug.sh
###run_ProDrug.sh###
gmx mdrun -deffnm dynamic -cpi dynamic.cpt -s dynamic.tpr -c dynamic_10µs.gro -noappend
nohup ./run_ProDrug.sh > run_ProDrug.out&

d. check the similation
check the finished time: tail run_ProDrug.out
check the simulate process: tail -f dynamic.part0003.log

4. Analyze
a. After simulation finished, download the .xtc .log .gro files from byrd03
creat the whole trajectory file
gmx trjcat -f dynamic.xtc dynamic.part0002.xtc -o prodrug_traj1.xtc

other script may be can use
gmx check -f prodrug_traj1.xtc

b. Analyze aggregation size distribution
gmx clustsize -f traj1_8.7us.xtc -s dynamic.tpr -mc maxclust.xvg -ac avcluste.xvg -nc nclust.xvg -cut 5 -n trjconv_stable.ndx -pbc

##wacth the movie.
vmd equilibration.gro, open prodrug_traj1.xtc;

c. Analyze the RMSD to proof whether the aggregation is stable.
#Convergence is also checked in terms of the structure, through the root mean square deviation (RMSD) against the starting structure and the average structure
gmx rms -s dynamic.tpr -f prodrug_traj1.xtc -o rmsd_xta1.xvg
xmgrace rmsd_xta1.xvg

7. Analyze the plateau of aggregate
a. Choose the stable time, put it in the centre of box
gmx trjconv -f traj2_10us.xtc -s dynamic.tpr -tu us -b 7.0 -e 15.0 -o traj2_10us.gro -pbc cluster

b. creat the index.ndx file of the biggest aggregation
gmx make_ndx -f traj2_10us.gro -o traj1.ndx
--a 24-46 | a 47-69 | a 93-115 | a 139-161 | a 323-345 | a 346-368 | a 392-414 | a 507-529 | a 530-552
--name 3 cluster1
--a 24-29
name 3 Gem1
--a 47-69
name 4 Gem2
--a 93-115
name 5 Gem3
--a 139-161

--a 323-345

--a 346-368

--a 392-414

--a 507-529

--a 530-552

c. generate the .xtc .gro fles of COM of Cluster1 ((not necessary)
gmx trjconv -f traj1_5us.xtc -s dynamic.tpr -n traj1.ndx -o whole1.gro -pbc whole

d. calculate the distance between COM of aggregation and Gems (not necessary)
   gmx traj -f traj1.7us.xtc -s cluster_1.7us.tpr -n traj1.7us.ndx -oxt COM_cluster.gro -com

seq 6 29 | gmx traj -f traj1.7us.xtc -s cluster_1.7us.tpr -n traj1.7us.ndx -oxt COM_Gem.gro -com -ng 24

seq 54 77 | gmx traj -f traj1.7us.xtc -s cluster_1.7us.tpr -n traj1.7us.ndx -oxt COM_End.gro -com -ng 24

e. Calculate the distance as function of time between COM of ggregation and each of Gems
gmx pairdist -f trjconv_stable.gro -s cluster.tpr -n trjconv_stable.ndx -o Gem_pairdist.xvg -selrpos whole_mol_com -seltype mol_com -pbc yes

cat gem | gmx pairdist -f trjconv_stable.gro -s cluster.tpr -n trjconv_stable.ndx -o Gem_pairdist.xvg -selrpos whole_mol_com -seltype mol_com -pbc yes

#calculate the rough distance by chimera#
calculate the distance between center of mass of cluster1 and Gem1 in one time, to make sure if it a good result.
chimera trjconv_cluster0.gro

f. Calculate the Radius of gyration of a molecule
gmx gyrate -s trjconv_stable.gro -f trjconv_stable.gro -o gyrate1.xvg -n trjconv_stable.ndx
or
gmx convert-tpr -s dynamic.tpr -o cluster.tpr
gmx gyrate -f trjconv_stable.gro -s cluster.tpr -n trjconv_stable.ndx -o gyrate1.xvg

g. Calculate the Radius distribution of Gem. Link. End; (COM of Clusters)
vi Gem-----edit the reference group, like 2
seq 30 53 >> Gem; put the calculate group in to Gem; like Gem group from 30 to 53
cat ../gem | gmx rdf -f traj1_7_15.xtc -s prodrug.tpr -n ../traj1.ndx -pbc yes -selrpos whole_mol_com -seltype res_com -bin 0.05 -o Gem_res.xvg

gmx rdf -f trjconv_stable.gro -s cluster.tpr -n trjconv_stable.ndx -pbc yes -selrpos whole_mol_com -seltype mol_com -bin 0.05 -o rdf_End.xvg

calculate the average of rdf distribution
gmx rdf -selrpos mol_com -seltype res_com -ref 'group 2' -sel 'group 2' -n traj1.ndx -o rdf_COM_Chains_r.xvg -f traj1_fin.xtc -s traj1_fin.tpr -bin 0.05 -rmax 5

gmx rdf -selrpos mol_com -seltype res_com -ref 'group 2' -sel 'group 78' -n traj1.ndx -o rdf_COM_Gem_r.xvg -f traj1_fin.xtc -s traj1_fin.tpr -bin 0.05 -rmax 5

gmx rdf -selrpos mol_com -seltype res_com -ref 'group 2' -sel 'group 79' -n traj1.ndx -o rdf_COM_PI_r.xvg -f traj1_fin.xtc -s traj1_fin.tpr -bin 0.05 -rmax 5

gmx rdf -selrpos mol_com -seltype res_com -ref 'group 2' -sel 'group 80' -n traj1.ndx -o rdf_COM_SG1_r.xvg -f traj1_fin.xtc -s traj1_fin.tpr -bin 0.05 -rmax 5

# compare the rdf distribution between COM of aggregate and Gem, PI, SG1, Amide, Water#
gmx rdf -selrpos mol_com -seltype res_com -ref -sel -n Water.ndx -o rdf_COM_compare.xvg -f traj1_15us.xtc -s ../dynamic.tpr -bin 0.05 -rmax 5 -b 7 -e 15 -tu us

choose group 6 as ref, 78, 79, 80, 81, 82, 3
in traj1.ndx
group 6, all the beads of aggregate
group 79, all the beads of Gem
group 80, al the beads of PI
group 81, all the beads of SG1
gourp 82, all the Amide
group 3, all the Water

Calculate the Radius distribution between COM of GEM, LINK, SG1
gmx rdf -selrpos res_com -seltype res_com -ref 'group 2' -sel 'group 2' -n traj1.ndx -o rdf_self_Chains.xvg -f traj1_fin.xtc -s traj1_fin.tpr -bin 0.05 -rmax 5

gmx rdf -selrpos res_com -seltype res_com -ref 'group 78' -sel 'group 78' -n traj1.ndx -o rdf_self_Gem.xvg -f traj1_fin.xtc -s traj1_fin.tpr -bin 0.05 -rmax 5

gmx rdf -selrpos res_com -seltype res_com -ref 'group 79' -sel 'group 79' -n traj1.ndx -o rdf_self_PI.xvg -f traj1_fin.xtc -s traj1_fin.tpr -bin 0.05 -rmax 5

gmx rdf -selrpos res_com -seltype res_com -ref 'group 80' -sel 'group 80' -n traj1.ndx -o rdf_self_SG1.xvg -f traj1_fin.xtc -s traj1_fin.tpr -bin 0.05 -rmax 5

I. calculate the minium distance between Gem/SG1 and Gem/SG1, chains and chains
gmx mindist -f traj1_fin.xtc -s traj1_fin.tpr -n traj1.ndx -on dist_mindist.xvg

or

gmx pairdist -f traj1_fin.xtc -s traj1_fin.tpr -n traj1.ndx -o dist5.xvg -selrpos atom -seltype atom

#### Gem_Gem.sh #####
#!/bin/bash

rm -rf Mini_GEMDISTRIBUTIONS
mkdir Mini_GEMDISTRIBUTIONS
rm -rf Mini_GEMDAT
mkdir Mini_GEMDAT

NGEM=29
IGEM=6
while [ $IGEM -lt $NGEM ]
    do
    seq $IGEM 29 >> Mini_GEMDAT/gem_$IGEM.dat
    cat Mini_GEMDAT/gem_$IGEM.dat | gmx pairdist -f traj2_7_15.xtc -s ../traj2.tpr -n ../../Anne_7to10/traj2.ndx -o Mini_GEMDISTRIBUTIONS/GEM_$IGEM.xvg -selrpos atom -seltype atom
    sed -i '/^\s*[@ s]/ d' Mini_GEMDISTRIBUTIONS/GEM_$IGEM.xvg
        rm -rf \#*
    let IGEM=$IGEM+1
    done
rm -rf Mini_GEMDAT
exit

###Gem_analys.sh###
#!/bin/bash
rm *dat
NGEM=29

for ((IGEM=6;IGEM<NGEM;IGEM++));
     do
     cp GEM_$IGEM.xvg GEM_$IGEM.dat
     awk '{print $1}' GEM_6.dat > GEM_6_dist.dat
     awk '{f=""; for (i=2; i<=NF; i++) f=f" "$i;} f!=last{print f;} {last=f;}' GEM_$IGEM.dat > GEM_d$IGEM.dat
     rm GEM_d27.dat
     awk '{print $2,$3}' GEM_27.dat > GEM_d27.dat
     awk '{print $2}' GEM_28.dat > GEM_d28.dat
    wc -l GEM_d*.dat
    paste GEM_6_dist.dat GEM_d*.dat > GEM_ALL2.xvg
    awk '{for (i=2;i<=NF; i++) print $1, $i}' GEM_ALL2.xvg > GEM_ALL_dist2.xvg
  done
rm *dat
exit

###Gem_SG1.sh###
#!/bin/bash

rm -rf Mini_GEM_SG1DISTRIBUTIONS
mkdir Mini_GEM_SG1DISTRIBUTIONS
rm -rf Mini_GEM_SG1DAT
mkdir Mini_GEM_SG1DAT

NGEM=29
for ((IGEM=6;IGEM<=NGEM;IGEM++));
    do
    seq $IGEM $IGEM >> Mini_GEM_SG1DAT/GEM_SG1_$IGEM.dat
    seq 54 77 >> Mini_GEM_SG1DAT/GEM_SG1_$IGEM.dat
    cat Mini_GEM_SG1DAT/GEM_SG1_$IGEM.dat | gmx pairdist -f traj2_7_15.xtc -s ../traj2.tpr -n ../../Anne_7to10/traj2.ndx -o Mini_GEM_SG1DISTRIBUTIONS/GEM_SG1_$IGEM.xvg -selrpos atom -seltype atom
    sed -i '/^\s*[@ s]/ d' Mini_GEM_SG1DISTRIBUTIONS/GEM_SG1_$IGEM.xvg
        rm -rf \#*
    done
rm -rf Mini_GEM_SG1DAT
exit

###Gem_SG1_analysis.sh###
#!/bin/bash

NGEM=29
for ((IGEM=6;IGEM<=NGEM;IGEM++));
     do
     cp GEM_SG1_$IGEM.xvg GEM_SG1_$IGEM.dat
     awk '{print $1}' GEM_SG1_6.dat > GEM_SG1_6_dist.dat
    awk '{print ($2,$3,$4,$5,$6,$7,$8,$9,$10,$11,$12,$13,$14,$15,$16,$17,$18,$19,$20,$21,$22,$23,$24,$25)}' GEM_SG1_$IGEM.dat > GEM_SG1_dd$IGEM.dat
    paste GEM_SG1_6_dist.dat GEM_SG1_dd* > GEM_SG1_ALL2.xvg
 wc -l GEM_SG1_dd*
    awk '{for (i=2;i<=NF; i++) print $1, $i}' GEM_SG1_ALL2.xvg > GEM_SG1_ALL_dist2.xvg
  done
rm *.dat
exit

###SG1_SG1.sh###
#!/bin/bash

rm -rf Mini_SG1DISTRIBUTIONS
mkdir Mini_SG1DISTRIBUTIONS
rm -rf Mini_SG1DAT
mkdir Mini_SG1DAT

NSG1=77
ISG1=54
while [ $ISG1 -lt $NSG1 ]
    do
    seq $ISG1 77 >> Mini_SG1DAT/SG1_$ISG1.dat
    cat Mini_SG1DAT/SG1_$ISG1.dat | gmx pairdist -f traj2_7_15.xtc -s ../traj2.tpr -n ../../Anne_7to10/traj2.ndx -o Mini_SG1DISTRIBUTIONS/SG1_$ISG1.xvg -selrpos atom -seltype atom
    sed -i '/^\s*[@ s]/ d' Mini_SG1DISTRIBUTIONS/SG1_$ISG1.xvg
        rm -rf \#*
    let ISG1=$ISG1+1
    done
rm -rf Mini_SG1DAT
exit

###SG1_SG1_analysis.sh###
#!/bin/bash
rm *dat
NGEM=77
for ((IGEM=54;IGEM<NGEM;IGEM++));
     do
     cp SG1_$IGEM.xvg SG1_$IGEM.dat
     awk '{print $1}' SG1_54.dat > SG1_54_dist.dat
     awk '{f=""; for (i=2; i<=NF; i++) f=f" "$i;} f!=last{print f;} {last=f;}' SG1_$IGEM.dat > SG1_d$IGEM.dat
     awk '{print $2}' SG1_76.dat > SG1_d76.dat
    wc -l SG1_d*.dat
    paste SG1_54_dist.dat SG1_d*.dat > SG1_ALL2.xvg
 awk '{for (i=2;i<=NF; i++) print $1, $i}' SG1_ALL2.xvg > SG1_ALL_dist2.xvg
  done
rm *dat
exit

###Chains.sh###
#!/bin/bash

rm -rf Mini_CHAINSDISTRIBUTIONS
mkdir Mini_CHAINSDISTRIBUTIONS
rm -rf Mini_CHAINSDAT
mkdir Mini_CHAINSDAT

NCHAINS=26
ICHAINS=3
while [ $ICHAINS -lt $NCHAINS ]
    do
    seq $ICHAINS 26 >> Mini_CHAINSDAT/CHAINS_$ICHAINS.dat
    cat Mini_CHAINSDAT/CHAINS_$ICHAINS.dat | gmx pairdist -f traj2_7_15.xtc -s ../traj2.tpr -n ../../Anne_7to10/Chains.ndx -o Mini_CHAINSDISTRIBUTIONS/CHAINS_$ICHAINS.xvg -selrpos atom -seltype atom
    sed -i '/^\s*[@ s]/ d' Mini_CHAINSDISTRIBUTIONS/CHAINS_$ICHAINS.xvg
        rm -rf \#*
    let ICHAINS=$ICHAINS+1
    done
rm -rf Mini_CHAINSDAT
exit

###Chains_analysis.sh###
#!/bin/bash
rm *dat
NCHAINS=25

for ((ICHAINS=3;ICHAINS<=NCHAINS;ICHAINS++));
     do
     cp CHAINS_$ICHAINS.xvg CHAINS_$ICHAINS.dat
     awk '{print $1}' CHAINS_3.dat > CHAINS_3_dist.dat
     awk '{f=""; for (i=2; i<=NF; i++) f=f" "$i;} f!=last{print f;} {last=f;}' CHAINS_$ICHAINS.dat > CHAINS_d$ICHAINS.dat

     awk '{print $2}' CHAINS_25.dat > CHAINS_d25.dat
    wc -l CHAINS_d*.dat
    paste CHAINS_3_dist.dat CHAINS_d*.dat > CHAINS_ALL2.xvg
   awk '{for (i=2;i<=NF; i++) print $1, $i}' CHAINS_ALL2.xvg > CHAINS_ALL_dist2.xvg
  done
rm *dat
exit
J. Solvent accessible surface area (SASA)
In order to study the drug release of polymer prodrugs, we compare the Solvent accessible surface of active points (Amide) in aggregate (contains 24 chains) and 1 chain (in octanol and in same calculate condition (water, WF and ions, same concentration of GemPi1kda)

For 24 chains aggregate
gmx sasa -f traj1_7_15.xtc -s prodrug.tpr -n ../traj1.ndx -o SAS_all.xvg -or RES_SAS_all.xvg -pbc -surface -output -ndots 25
GemPi1kda as surface
Gem, PI, SG1, Amide as output

SAS_all.xvg is the All SAS distribute as function of times
RES_SAS_all.xvg is the average SAS distribution as function of chains
For 1 chain calculation
1. 1chain in octanol (jarre, 6h)
:~/GemPi1kDa/byrd03/octanol/Take6_ok/test_sasa
~/ProDrug/GemPi1kDa/byrd03/solution/Gem24/trajectory/1chain_octanol

#increase the calculate time until 1 us#
gmx convert-tpr -s cg_md.tpr -o cg_md_1.tpr -until 1000000
gmx mdrun -s cg_md_1.tpr -v -deffnm cg_md

Analysis
#SASA#
gmx sasa -f cg_md_1.xtc -s cg_md_1.tpr -n cg_md.ndx -o 1chain_oct_sasa.xvg -or 1chain_oct_res_sas.xvg -pbc -surface -output -ndots 25

#Average#
awk '{sum+=sprintf("%f",$5)}END{printf "%.6f\n%.6f\n",sum,sum/NR}' 1chain_W_sasa.xvg

2. 1chain in water ( byrd02, 3h)
~/ProDrug/GemPi1kDa/byrd03/solution/Gem24/trajectory/1chain_water
conditions:
- 150mM NaCl + water
- 1mM ProDrug (1kda)
- 1microsecond expected
- same cg_md.itp file in octanol

Copy cg_md.xtc, cg_md.tpr, 1kda_mapped.itp from ~/ProDrug/Octanol/Take6_ok

#creat prodrug gro file#
gmx trjconv -f cg_md.xtc -s cg_md.tpr -o prodrug.gro

# Place the solute in a simulation box
gmx editconf -f prodrug.gro -bt cubic -d 1 -o prodrug_inbox.gro

# define the size of box
gmx editconf -f prodrug_inbox.gro -o system_temp.gro -d 1.0 -bt cubic -box 11.84 11.84 11.84

# Minimization in vaccum following by minimization in solution
gmx grompp -f minimization-vac.mdp -c system_temp.gro -p system.top -o minimization-vac.tpr
gmx mdrun -deffnm minimization-vac -v

# Solvatation
gmx solvate -cp minimization-vac.gro -cs water.gro -radius 0.21 -o system_W.gro

gmx grompp -f ions.mdp -c system_W.gro -p system.top -o ions.tpr

# Add ions into the box
gmx genion -s ions.tpr -p system.top -neutral -conc 0.15 -pname NA+ -nname CL- -o system_WI.gro
Then select the water group, here it’s the #3.

# Add anti-freeze water into the box
Gempi1kda 1
;W 13115
W 11533
WF 1282
NA+ 150
CL - 150

change the last 1282 W to WF in system_WI.gro

# minimization
gmx grompp -f minimization.mdp -c system_WI.gro -p system_2.top -o minimization.tpr -maxwarn 1
gmx mdrun -deffnm minimization -v

#define the set in equilibration.mdp#
vi equilibration.mdp, check the set as below;
tc-grps = ProDrug Solvent

gmx make_ndx -f minimization.gro -o system.ndx
name 2(1kda) ProDrug
3(W) | 4(WF) | 5(ION)
name 6 Solvent

# Equil
gmx grompp -f equilibration.mdp -c minimization.gro -p system.top -o equilibration.tpr -n system.ndx

gmx mdrun -deffnm equilibration -v

# Prod
gmx grompp -f dynamic.mdp -c equilibration.gro -p system.top -o dynamic.tpr -n system.ndx
gmx mdrun -deffnm dynamic -v

Analysis
#SASA#
gmx sasa -f dynamic.xtc -s dynamic.tpr -n 1chain.ndx -o 1chain_W_sasa.xvg -or 1chain_W_res_sas.xvg -pbc -surface -output -ndots 25

#Average#
awk '{sum+=sprintf("%f",$5)}END{printf "%.6f\n%.6f\n",sum,sum/NR}' 1chain_W_sasa.xvg

k. Analyze the average rdf distribution (Tap said is not a good method, but script can use for another things)
#cp part4_rdf_Gem_mol.xvg part4_rdf_Gem_mol.dat
#vi part4_rdf_Gem_mol.dat

Read the values of columns from 2nd to 17th in rdf_Gem.dat
awk '{print ($2+$3+$4+$5+$6+$7+$8+$9+$10+$11+$12+$13+$14+$15+$16+$17+$18+$19+$20+$21+$22+$23+$24+$25)}' rdf_Gem.dat

Calculate the average value of columns from 2nd to 17th , then output into rdf_gem_average.dat
awk '{print ($2+$3+$4+$5+$6+$7+$8+$9+$10+$11+$12+$13+$14+$15+$16+$17+$18+$19+$20+$21+$22+$23+$24+$25)/24}' rdf_Gem.dat > rdf_Gem_average.dat

output the value of 1st columns to rdf_gem_dist.dat
awk '{print $1}' part4_rdf_Gem_mol.dat > rdf_gem_dist.dat

check the columns of two files
wc -l rdf_End_average.dat rdf_End_dist.dat

combine two .dat files into one .dat file
paste rdf_End_dist.dat rdf_End_average.dat > rdf_End_dist_average.dat

open the file, check the results
xmgrace rdf_gem_dist_average.dat